## Slide 1
KJEI’s, Trinity Academy of Engineering
Department of Electronics and
Telecommunication Engineering
Academic Year 2026–27 Semester I
Project Review 3
1
    Name of Students
    Dhanesh Chaudhari (4114)
    Yash Ahire (4101)
    Mrudula Pagar (____)
    Ujjwal Kshirsagar (____)
Date: 3 October 2026
WattSense
Energy Signature Analysis and Battery Runtime Estimation
Under the guidance of
Mahesh Sapte
Group 7
Notes: The main project focus is energy-signature analysis, load-energy estimation and battery-runtime estimation. Group 7 and guide Mahesh Sapte were confirmed on 3 October 2026. The two unconfirmed roll numbers are intentionally blank. This title replaces the earlier priority-load demonstration framing for this review; existing code and hardware have not been changed by preparing these slides.
Sources
User steering and confirmed team details, 3 October 2026
sih 2026 shubham.pptx

## Slide 2
2
Introduction and Topic Overview
An energy signature is a load’s measured current and power pattern over time.
Battery percentage alone does not explain how device use changes backup time.
WattSense will learn profiles of selected DC loads and estimate their energy use.
Available battery energy and load demand will produce a runtime estimate.
Applications include portable DC equipment and renewable-energy demonstrators.
Review 3: monitoring software and PCB design prepared.
Next stage: signature data, classification and measured validation.
Notes: The restored SIH USP is signature-based load detection and energy estimation linked to battery backup. Signature matching and the dataset remain proposed work. The present monitoring foundation comprises firmware, synthetic demonstration, charge/runtime software, local logging and a routed four-layer PCB. The prototype scope is selected known DC loads; the current PCB does not directly measure household AC appliances. Automatic matching after initial training differs from universal zero-configuration recognition. No classifier accuracy or physical energy/runtime measurement is currently available.
Sources
sih 2026 shubham.pptx
firmware/include/controller.h
wattsense/server.py

## Slide 3
3
Literature Survey 1 of 4
No | Author, Year | Problem | Method | Data / tests | Finding | Scope limit
1 | Athanasiadis et al. 2021 | Load energy estimation | Events + CNN + power estimate | Reported experimental evaluation | Real-time consumption estimates | Transient data needed
2 | Mollel et al. 2023 | Unclear load classification | Decision trees + explanations | REFIT to UK-DALE transfer tests | Feature selection improves classification | Cross-house transfer needs testing
3 | Jaime et al. 2026 | Variable evaluation methods | PRISMA + meta-analysis | 30 studies; 2017-2024 publications | Performance varies across study settings | Heterogeneous study methods
4 | Xiang et al. 2026 | Practical deployment barriers | Event/state methods; scenario review | Review of published NILM studies | Maps deployment needs and trade-offs | Unknown loads and transfer limits
5 | Li et al. 2026 | Similar load signatures | AC V-I + dual-branch network | PLAID AC appliance recordings | Feature fusion aids classification | No AC waveforms from INA219
Energy signatures and load estimation
Notes: These papers inform the proposed project. Findings belong to the cited authors and are not WattSense results. Scope limits describe applicability to our small DC prototype.
[1] Christos Athanasiadis, Dimitrios Doukas, Theofilos Papadopoulos, Antonios Chrysopoulos, "A Scalable Real-Time Non-Intrusive Load Monitoring System for the Estimation of Household Appliance Power Consumption", Energies, vol. 14, no. 3, Art. 767, 2021, doi: 10.3390/en14030767.
https://www.mdpi.com/1996-1073/14/3/767
Evidence: Primary publisher abstract states three blocks: event detection, CNN classifier and power estimator using active-power turn-on transients. It reports computational/memory efficiency qualitatively. Cached full-page excerpt ends within the introduction, so dataset names, exact sampling rates and numerical performance are not asserted. The limitation cell is an applicability inference: this method needs suitable transient measurements and an already trained target-appliance classifier. It does not validate WattSense, universal detection or zero-configuration deployment.
[2] Rachel Stephen Mollel, Lina Stankovic, Vladimir Stankovic, "Explainability-Informed Feature Selection and Performance Prediction for Nonintrusive Load Monitoring", Sensors, vol. 23, no. 10, Art. 4845, 2023, doi: 10.3390/s23104845.
https://www.mdpi.com/1424-8220/23/10/4845
Evidence: Publisher abstract describes interpretable decision-tree classification, local/global feature importance, REFIT training and unseen same-house/UK-DALE-house evaluation. It reports class-specific improvements, but the displayed row deliberately transfers no percentage to WattSense. Cross-house transfer testing is a design implication drawn from the study setting; the current DC INA219 system cannot inherit its household-data performance.
[3] Herman Cristiano Jaime, Adler Diniz de Souza, Raphael Carlos Santos Machado, Otávio de Souza Martins Gomes, "Machine Learning Models for Non-Intrusive Load Monitoring: A Systematic Review and Meta-Analysis", Inventions, vol. 11, no. 2, Art. 29, 2026, doi: 10.3390/inventions11020029.
https://www.mdpi.com/2411-5134/11/2/29
Evidence: This is a systematic review and meta-analysis, not a new hardware trial. The publisher abstract states 30 eligible studies, random-effects pooling of F1 scores and substantial heterogeneity. Hybrid models had high pooled scores with limited study support; traditional models had broader validation. No pooled score is used as a WattSense result. Issue citation year is 2026; covered primary-study period is 2017-2024.
[4] Haotian Xiang, Wenjing Su, Yi Zong, "Non-Intrusive Load Monitoring: A Systematic Review of Methods, Scenario-Specific Challenges, and Pathways to Practical Deployment", Energies, vol. 19, no. 8, Art. 1883, 2026, doi: 10.3390/en19081883.
https://www.mdpi.com/1996-1073/19/8/1883
Evidence: This is a systematic review/framework, not new hardware validation. Its abstract explicitly identifies real-time/accuracy trade-offs, privacy, unknown loads, behaviour modelling, data quality, transferability, integration and cost. The row is a qualitative synthesis and does not assert a dataset, new classifier or measured accuracy for this review. Relevant to scoping a small known-load prototype with an unknown/ambiguous output.
[5] Yiran Li, Yan Li, Peng Han, "A Non-Intrusive Load Identification Method Based on the Fusion of Steady-State Features and Lightweight Network", Energies, vol. 19, no. 13, Art. 3131, 2026, doi: 10.3390/en19133131.
https://www.mdpi.com/1996-1073/19/13/3131
Evidence: Publisher abstract describes V-I trajectory images plus active/reactive power, trajectory area and slope, fused with a lightweight dual-branch network. Evaluation uses PLAID. The original abstract reports 95.35% recognition accuracy and 0.17M parameters, but these external results are not displayed or attributed to WattSense. This is an AC waveform-based method: the current INA219 DC voltage/current telemetry does not provide synchronised AC V-I trajectories, reactive power or waveform images. The limitation is an explicit sensor/method applicability comparison, not a defect demonstrated by the paper.
Sources

## Slide 4
4
Literature Survey 2 of 4
No | Author, Year | Problem | Method | Data / tests | Finding | Scope limit
6 | Movassagh et al. 2021 | Accumulated SOC error | Analytical error decomposition | Error models and simulations | Quantifies four SOC error sources | Current and initial-SOC errors
7 | Zhang et al. 2018 | Changing battery model parameters | Decoupled weighted RLS | Lithium-ion cell measurements | Separates fast / slow dynamics | Actual pack characterisation needed
8 | Gismero et al. 2020 | Charge drift and capacity aging | Coulomb counting, OCV reset, RLS | Aged NMC cells; dynamic loads | OCV resets limit accumulated drift | Rest time and chemistry matter
9 | Yang et al. 2021 | SOC and parameter coupling | Separated RLS + EKF | 18650 data at varied temperature | Lower error than conventional RLS | Needs characterized model and data
10 | Rzepka et al. 2021 | Empirical tuning and sensor noise | Circuit + hysteresis + EKF tuning | Cell estimator experiment | Tuning improves estimator stability | Needs noise estimates
Battery state-of-charge estimation
Notes: These papers inform the proposed project. Findings belong to the cited authors and are not WattSense results. Scope limits describe applicability to our small DC prototype.
[6] K. Movassagh, A. Raihan, B. Balasingam, and K. Pattipati, "A Critical Look at Coulomb Counting Approach for State of Charge Estimation in Batteries," Energies, vol. 14, no. 14, Art. 4074, 2021, doi: 10.3390/en14144074.
https://doi.org/10.3390/en14144074
Evidence: Separates current-measurement, integration, capacity and timing errors. Its results do not establish a WattSense SOC accuracy figure. Calibration/initialization is our design implication.
[7] C. Zhang, W. Allafi, Q. Dinh, P. Ascencio, and J. Marco, "Online estimation of battery equivalent circuit model parameters and state of charge using decoupled least squares technique," Energy, vol. 142, pp. 678–688, 2018, doi: 10.1016/j.energy.2017.10.043.
https://doi.org/10.1016/j.energy.2017.10.043
Evidence: Published in 2018 despite 2017 in DOI. Supports caution about fixed assumed plant parameters. WattSense has not implemented this estimator or measured its pack parameters.
[8] A. Gismero, E. Schaltz, and D.-I. Stroe, "Recursive State of Charge and State of Health Estimation Method for Lithium-Ion Batteries Based on Coulomb Counting and Open Circuit Voltage," Energies, vol. 13, no. 7, Art. 1811, 2020, doi: 10.3390/en13071811.
https://doi.org/10.3390/en13071811
Evidence: Tested aged cells with changing current/temperature. The paper explicitly identifies insufficient relaxation as a capacity-estimation issue. Our LFP pack cannot inherit its NMC OCV map or accuracy.
[9] K. Yang, Y. Tang, and Z. Zhang, "Parameter Identification and State-of-Charge Estimation for Lithium-Ion Batteries Using Separated Time Scales and Extended Kalman Filter," Energies, vol. 14, no. 4, Art. 1054, 2021, doi: 10.3390/en14041054.
https://doi.org/10.3390/en14041054
Evidence: The result is specific to its datasets and estimator. It informs future characterization; WattSense currently uses a simpler current-integration policy, not the published RLS/EKF method.
[10] B. Rzepka, S. Bischof, and T. Blank, "Implementing an Extended Kalman Filter for SoC Estimation of a Li-Ion Battery with Hysteresis: A Step-by-Step Guide," Energies, vol. 14, no. 13, Art. 3733, 2021, doi: 10.3390/en14133733.
https://doi.org/10.3390/en14133733
Evidence: Conclusions compare systematic and rough filter tuning. This is a future-estimator reference, not evidence that WattSense's INA219/current integration achieves the paper's accuracy.
Sources

## Slide 5
5
Literature Survey 3 of 4
No | Author, Year | Problem | Method | Data / tests | Finding | Scope limit
11 | Zine et al. 2022 | Simple real-time SOC estimation | Current integration | Lead-acid bench tests | Bench SOC workflow | LFP tests still needed
12 | Fahmy et al. 2023 | SOC with changing conditions | Coulomb counting plus adaptive UKF | 2.6 Ah Panasonic simulations | Lower simulated error in comparisons | Numerical results only
13 | Wang et al. 2023 | LFP plateau and temperature | Temperature ECM; improved EKF | LFP chamber / load tests | Temperature-aware estimate | Needs pack-specific data
14 | Turkmanović et al. 2024 | Estimator energy versus accuracy | Two EKFs at varied rates | PC accuracy + STM32H7 timing | Sample-rate trade-off | ESP32 timing unknown
15 | Bampi et al. 2025 | Battery parameter testing | Electronic load + ECM / EKF | LTO cell + ESP32 rig | Parameter and SOC estimates | Different test rig
Battery measurement and validation
Notes: These papers inform the proposed project. Findings belong to the cited authors and are not WattSense results. Scope limits describe applicability to our small DC prototype.
[11] B. Zine, H. Bia, A. Benmouna, M. Becherif, and M. Iqbal, "Experimentally Validated Coulomb Counting Method for Battery State-of-Charge Estimation under Variable Current Profiles," Energies, vol. 15, no. 21, Art. 8172, 2022, doi: 10.3390/en15218172.
https://doi.org/10.3390/en15218172
Evidence: The broad Li-ion discussion in the abstract must not be mistaken for our 4S LFP validation. Initial SOC and suitable measurements are needed; this study is a practical procedure reference.
[12] Hend M. Fahmy, Rania A. Swief, Hany M. Hasanien, Mohammed Alharbi, José Luis Maldonado, and Francisco Jurado, "Hybrid State of Charge Estimation of Lithium-Ion Battery Using the Coulomb Counting Method and an Adaptive Unscented Kalman Filter", Energies, vol. 16, no. 14, Art. 5558, 2023, doi: 10.3390/en16145558.
https://doi.org/10.3390/en16145558
Evidence: The abstract explicitly labels numerical simulations and describes parameter fitting with African Vultures Optimization. The table includes only the estimator core. Do not present this as a physical WattSense comparison.
[13] M. Wang, G. Wang, Z. Xiao, Y. Sun, and Y. Zheng, "State of Charge Estimation of LiFePO4 in Various Temperature Scenarios," Batteries, vol. 9, no. 1, Art. 43, 2023, doi: 10.3390/batteries9010043.
https://doi.org/10.3390/batteries9010043
Evidence: Direct chemistry relevance. Temperature-dependent capacity and the flat OCV region motivate measuring the actual pack instead of relying on the assumed teaching curve. WattSense's fixed-temperature simulation does not reproduce these tests.
[14] H. Turkmanović, I. Popović, and V. Rajović, "Toward Energy Efficient Battery State of Charge Estimation on Embedded Platforms," Electronics, vol. 13, no. 21, Art. 4256, 2024, doi: 10.3390/electronics13214256.
https://doi.org/10.3390/electronics13214256
Evidence: Contrasts Rint and second-order RC EKFs and connects estimator rate to energy cost. Its reported savings cannot be copied to the ESP32; our 0.8 W controller load remains an assumption awaiting measurement.
[15] S. Bampi, G. Waltrich, and A. Vaccari, "Electronic Load for Parameter Characterization in Equivalent Circuit Models of Lithium-Ion Batteries," Eletrônica de Potência, vol. 30, Art. e202521, 2025, doi: 10.18618/REP.e202521.
https://doi.org/10.18618/REP.e202521
Evidence: Publisher full-text reports an ESP32 electronic-load instrument, lithium-titanate cell characterisation and EKF SOC estimation. Useful evidence for a laboratory procedure and embedded integration. Its battery chemistry, electronic-load instrument and estimator differ from the current protected-LFP/INA219 WattSense design; none of its accuracy transfers to our project.
Sources

## Slide 6
6
Literature Survey 4 of 4
No | Author, Year | Problem | Method | Data / tests | Finding | Scope limit
16 | Marahatta et al. 2021 | Limited rural energy supply | Priority switching + SCADA | Laboratory solar-battery microgrid | Maintains essential-load service | Three-level solar system
17 | Rajbhandari et al. 2024 | Variable solar supply | Day-ahead forecasts + PSO | Generation/load simulations | Improves priority-load continuity | Requires forecasts and optimisation
18 | Guo & Kors 2021 | Renewable energy teaching | Sensors, Raspberry Pi, SCADA | Outdoor rig + student tests | Integrated educational platform | Educational; no load estimator
19 | Yusubov & Bekirova 2023 | Variable PV output and demand | Power/SOC rules + load shedding | Standalone DC microgrid simulations | Coordinates loads within SOC bounds | No physical validation reported
20 | Basantes et al. 2023 | Dispatch cost and battery limits | Hierarchical control + MPC | Simulink + FICO Xpress scenarios | Reduces simulated operating cost | Battery degradation model deferred
Monitoring and energy-management integration
Notes: These papers inform the proposed project. Findings belong to the cited authors and are not WattSense results. Scope limits describe applicability to our small DC prototype.
[16] A. Marahatta, Y. Rajbhandari, A. Shrestha, A. Singh, A. Gachhadar, and A. Thapa, 'Priority-based low voltage DC microgrid system for rural electrification,' Energy Reports, vol. 7, pp. 43-51, 2021, doi: 10.1016/j.egyr.2020.11.030.
https://www.sciencedirect.com/science/article/pii/S2352484720314554
Evidence: Publisher explicitly describes experimental analysis and a low-cost SCADA implementation. Saved evidence identifies three load priorities and battery thresholds. This is close prior art, so priority shedding itself is not a new WattSense algorithm. The row states a qualitative study finding and transfers no performance percentage.
[17] Y. Rajbhandari, A. Marahatta, A. Shrestha, A. Gachhadar, A. Thapa, F. Gonzalez-Longatt, and P. Korba, 'Enhanced demand side management for solar-based isolated microgrid system: Load prioritisation and energy optimisation,' IET Smart Grid, vol. 7, no. 3, pp. 294-313, 2024, doi: 10.1049/stg2.12151.
https://ietresearch.onlinelibrary.wiley.com/doi/10.1049/stg2.12151
Evidence: Primary discussion identifies stochastic load/generation simulations, three priority levels and PSO-optimised SOC shedding points using forecasts. Cite issue year 2024 rather than online-first 2023. WattSense has not implemented or evaluated this forecasting/PSO method; the row is external context and transfers no result.
[18] L. Guo and J. Kors, Jr., 'Design of a Laboratory Scale Solar Microgrid Cyber-Physical System for Education,' Electronics, vol. 10, no. 13, Art. 1562, 2021, doi: 10.3390/electronics10131562.
https://www.mdpi.com/2079-9292/10/13/1562
Evidence: Primary paper reports a solar panel, purchased MPPT controller, rechargeable battery, relay-controlled loads and student assessment. Hardware data were sampled every ten minutes in its reported outdoor run. Its focus is educational system integration; it does not establish the proposed WattSense signature estimator or any WattSense measurement.
[19] E. Yusubov and L. Bekirova, 'A standalone DC microgrid energy management strategy using the battery state of charge,' Informatyka, Automatyka, Pomiary w Gospodarce i Ochronie Środowiska, vol. 13, no. 3, pp. 75-78, 2023, doi: 10.35784/iapgos.5320.
https://ph.pollub.pl/index.php/iapgos/en/article/view/5320
Evidence: The publisher abstract explicitly combines available-source power, demand and SOC with load-shedding capability and evaluates an algorithm by simulation. Although authors claim battery-life benefits, the row deliberately uses SOC-limit coordination and does not present lifetime extension as measured cycling data.
[20] J. A. Basantes, D. E. Paredes, J. R. Llanos, D. E. Ortiz, and C. D. Burgos, 'Energy Management System (EMS) Based on Model Predictive Control (MPC) for an Isolated DC Microgrid,' Energies, vol. 16, no. 6, Art. 2912, 2023, doi: 10.3390/en16062912.
https://www.mdpi.com/1996-1073/16/6/2912
Evidence: Metadata/byline was confirmed from the primary published PDF hosted in a research repository. The study compares with/without EMS under radiation and demand disturbances. Its conclusions explicitly defer battery-degradation modeling and diesel-start constraints to future work. Real-time feedback here is within the simulated coupled control system; do not call it real hardware measurement.
Sources

## Slide 7
7
Research Gap / Problem Identification
Published recognition results depend on sensors, sampling rate and dataset.
Similar load profiles and unseen devices can make identification uncertain.
Runtime also depends on usable capacity, charge reference and actual demand.
A low-cost DC prototype must evaluate the complete measurement chain.
Our focus is signature matching with uncertainty, energy estimates and runtime error.
Proposed contribution: connect measured load behaviour with available battery energy.
Notes: Priority switching and NILM are established prior work. The contribution is a reproducible student implementation and evaluation of a known-load DC prototype, not a new universal recognition algorithm. Classifier outputs need UNKNOWN/ambiguous rejection. Similar patterns, combinations, converter efficiency and controller overhead may limit identification and energy attribution. Battery-runtime estimates depend on a valid starting reference and independently established capacity. The present INA219 acquisition chain does not capture AC voltage-current trajectories, reactive power or high-frequency harmonics.
Sources
literature.json: Athanasiadis, Mollel, Xiang and Li sources
firmware/src/main.cpp
docs/TEST_PLAN.md

## Slide 8
8
Problem Statement
Objectives
Develop a battery-powered DC system that uses measured electrical profiles to estimate load energy consumption and battery runtime, while reporting uncertainty for unrecognised loads.
Acquire and calibrate battery/load measurements.
Build a labelled signature dataset for selected DC loads.
Compare feature matching and a classifier with unknown rejection.
Estimate charge, energy use and runtime under stated usage.
Evaluate errors using independent recording sessions.
Notes: The work starts with a small known-load library. A signature consists of slow current/power changes and behaviour, not a unique guaranteed fingerprint. Recognition, energy estimation and runtime estimation are separate evaluation tasks. Labels and independent instruments are needed for ground truth. No numeric recognition target is presented as an achieved score. A profile-based estimate states its usage scenario; a battery percentage alone cannot determine duration.
Sources
User USP correction, 3 October 2026
docs/TEST_PLAN.md

## Slide 9
9
Proposed System Architecture
Protected battery, regulated DC supply and selected compatible loads
Sensing PCB
Current / voltage
Temperature
ESP32
Calibration and
raw measurements
Signature engine
Features and
profile / UNKNOWN
USB serial
Load-energy estimate
Power, state, duration
Energy and runtime
SOC + usable Wh
+ demand estimate
Local dashboard
Estimates and CSV
Foundation: sensing firmware, charge/runtime software, dashboard and Rev B CAD.
Proposed: raw signature logging, trained profiles and profile-based estimates.
Notes: This is an information-flow diagram, not a wiring diagram. Sensor U1 measures net battery current; U2 measures aggregate converter-input/load demand; U3 is a charging-input channel initially disabled. Individual appliance current is not directly measured by three separate appliance sensors. Selected known-load training uses controlled sessions on the same measurement path. Estimate attributable load energy with reference measurements and consistent converter/controller overhead; do not equate converter-input energy with appliance-terminal energy without calibration. The first signature engine will run in local Python. Firmware currently samples nominally 10 Hz but emits JSON at approximately 1 Hz, so a qualified raw-rate logger must be implemented. Use slow/event features appropriate to verified sampling, not harmonic fingerprints. SOC needs a legitimate full reference and capacity basis; it starts unknown. Existing hardware outputs remain disabled until staged qualification. The four-layer 100 x 90 mm PCB is designed, not assembled. Purchased BMS/charger retain their own protection and charge regulation duties.
Sources
hardware/REFERENCE_WIRING.md
firmware/src/main.cpp
firmware/include/controller.h
docs/LAB_START_GUIDE.md

## Slide 10
10
Dataset / Data Collection
Data item | Collection plan
Initial scope | 4–6 known compatible DC load types, one per run
Recorded fields | Time, voltage, current, power, device label and state
Conditions | Repeated sessions, battery levels and operating states
Features | Power steps, mean, variation, slope and duration
Train / test split | Separate complete sessions, then test combinations
Nominal acquisition: 10 Hz. Current telemetry: approximately 1 Hz.
Add and qualify raw logging before collecting signature features.
Physical signature records are the next stage.
Existing synthetic records support development and demonstration.
Notes: There is no measured signature dataset at present. Start with 4–6 load types whose voltage and current are compatible with the actual converter and PCB limits; exact products have not been selected. Record the true device/state and sample timing. First use one load, then held-out combinations and unseen loads. Split by complete session, preferably across battery levels, rather than neighbouring windows from the same recording. Record source=measured or simulated, instrument calibration, converter conditions and controller supply arrangement. The selected feature set must reflect actual timing and sensor bandwidth; 1 Hz CSV data cannot validate short startup features. Aggregate demand alone may not separate similar devices. Unknown/ambiguous outcomes are required.
Sources
firmware/src/main.cpp
wattsense/server.py
docs/TEST_PLAN.md
literature.json: Mollel and Xiang sources

## Slide 11
11
Expected Outcomes and Evaluation
Expected output | Evaluation method
Known-load matching | Confusion matrix and macro F1 on held-out sessions
Unknown indication | Unknown detection and false acceptance
Consumed-energy estimate | Estimated Wh against independent reference energy
Battery-runtime estimate | Absolute error in minutes and percentage error
Trustworthy measurements | Calibration errors and missing-data handling
Foundation audit: 45 Python tests, 67 host C++ assertions.
Both ESP32 firmware targets compile.
Signature recognition and physical estimation accuracy
will be established through measured tests.
Notes: The test counts are from the 30 September 2026 foundation audit and do not validate a signature classifier. Recognition metrics apply only after a labelled dataset exists. Report macro F1/confusion matrices and unseen-device false acceptance separately. Compare energy at the same physical measurement point, accounting for reference uncertainty. Compute power from calibrated voltage and current and integrate with actual sample timing. Runtime estimates should be compared against independently observed normal discharge endpoints under defined usage profiles, with repeated runs. Use the measured usable battery energy rather than treating nominal voltage x capacity as exact. Percentage runtime error is meaningful only for non-zero reference durations. No classifier score, energy savings percentage or household compatibility is claimed.
Sources
docs/RECHECK_2026-09-30.md
docs/TEST_PLAN.md
simulations/hardware-assumptions.json

## Slide 12
12
Project Timeline
Period | Work and milestone
September 2026 | Foundation prepared: firmware, dashboard, CAD and models
October 2026 | Assemble, calibrate and implement raw signature logging
November 2026 | Record labelled sessions and compare matching methods
Dec 2026–Jan 2027 | Validate load-energy and battery-runtime estimates
Feb–Mar 2027 | Repeat tests, analyse errors and prepare final demonstration
Review 3: 3 October 2026
Final submission: the department’s next-semester schedule
Notes: These months are proposed planning stages, not confirmed delivery dates or completed activity. The user places final submission next semester. The restored signature USP requires dataset collection and new analysis software; prior firmware/software tests cover the monitoring foundation. The existing INR 9,700 allocation has not been confirmed by delivered quotes and does not fund a re-spin or solar purchase. Keep core DC scope practical. No hardware, classifier or cloud module has been created by this deck.
Sources
User scope correction, 3 October 2026
docs/NEXT_STEPS.md
hardware/BUYING_PLAN_PUNE.md

## Slide 13
13
References
[1] Athanasiadis et al., 2021
10.3390/en14030767
[2] Mollel et al., 2023
10.3390/s23104845
[3] Jaime et al., 2026
10.3390/inventions11020029
[4] Xiang et al., 2026
10.3390/en19081883
[5] Li et al., 2026
10.3390/en19133131
[6] Movassagh et al., 2021
10.3390/en14144074
[7] Zhang et al., 2018
10.1016/j.energy.2017.10.043
[8] Gismero et al., 2020
10.3390/en13071811
[9] Yang et al., 2021
10.3390/en14041054
[10] Rzepka et al., 2021
10.3390/en14133733
[11] Zine et al., 2022
10.3390/en15218172
[12] Fahmy et al., 2023
10.3390/en16145558
[13] Wang et al., 2023
10.3390/batteries9010043
[14] Turkmanović et al., 2024
10.3390/electronics13214256
[15] Bampi et al., 2025
10.18618/REP.e202521
[16] Marahatta et al., 2021
10.1016/j.egyr.2020.11.030
[17] Rajbhandari et al., 2024
10.1049/stg2.12151
[18] Guo & Kors, 2021
10.3390/electronics10131562
[19] Yusubov & Bekirova, 2023
10.35784/iapgos.5320
[20] Basantes et al., 2023
10.3390/en16062912
Notes: [1] Christos Athanasiadis, Dimitrios Doukas, Theofilos Papadopoulos, Antonios Chrysopoulos, "A Scalable Real-Time Non-Intrusive Load Monitoring System for the Estimation of Household Appliance Power Consumption", Energies, vol. 14, no. 3, Art. 767, 2021, doi: 10.3390/en14030767.
https://www.mdpi.com/1996-1073/14/3/767
Evidence: Primary publisher abstract states three blocks: event detection, CNN classifier and power estimator using active-power turn-on transients. It reports computational/memory efficiency qualitatively. Cached full-page excerpt ends within the introduction, so dataset names, exact sampling rates and numerical performance are not asserted. The limitation cell is an applicability inference: this method needs suitable transient measurements and an already trained target-appliance classifier. It does not validate WattSense, universal detection or zero-configuration deployment.
[2] Rachel Stephen Mollel, Lina Stankovic, Vladimir Stankovic, "Explainability-Informed Feature Selection and Performance Prediction for Nonintrusive Load Monitoring", Sensors, vol. 23, no. 10, Art. 4845, 2023, doi: 10.3390/s23104845.
https://www.mdpi.com/1424-8220/23/10/4845
Evidence: Publisher abstract describes interpretable decision-tree classification, local/global feature importance, REFIT training and unseen same-house/UK-DALE-house evaluation. It reports class-specific improvements, but the displayed row deliberately transfers no percentage to WattSense. Cross-house transfer testing is a design implication drawn from the study setting; the current DC INA219 system cannot inherit its household-data performance.
[3] Herman Cristiano Jaime, Adler Diniz de Souza, Raphael Carlos Santos Machado, Otávio de Souza Martins Gomes, "Machine Learning Models for Non-Intrusive Load Monitoring: A Systematic Review and Meta-Analysis", Inventions, vol. 11, no. 2, Art. 29, 2026, doi: 10.3390/inventions11020029.
https://www.mdpi.com/2411-5134/11/2/29
Evidence: This is a systematic review and meta-analysis, not a new hardware trial. The publisher abstract states 30 eligible studies, random-effects pooling of F1 scores and substantial heterogeneity. Hybrid models had high pooled scores with limited study support; traditional models had broader validation. No pooled score is used as a WattSense result. Issue citation year is 2026; covered primary-study period is 2017-2024.
[4] Haotian Xiang, Wenjing Su, Yi Zong, "Non-Intrusive Load Monitoring: A Systematic Review of Methods, Scenario-Specific Challenges, and Pathways to Practical Deployment", Energies, vol. 19, no. 8, Art. 1883, 2026, doi: 10.3390/en19081883.
https://www.mdpi.com/1996-1073/19/8/1883
Evidence: This is a systematic review/framework, not new hardware validation. Its abstract explicitly identifies real-time/accuracy trade-offs, privacy, unknown loads, behaviour modelling, data quality, transferability, integration and cost. The row is a qualitative synthesis and does not assert a dataset, new classifier or measured accuracy for this review. Relevant to scoping a small known-load prototype with an unknown/ambiguous output.
[5] Yiran Li, Yan Li, Peng Han, "A Non-Intrusive Load Identification Method Based on the Fusion of Steady-State Features and Lightweight Network", Energies, vol. 19, no. 13, Art. 3131, 2026, doi: 10.3390/en19133131.
https://www.mdpi.com/1996-1073/19/13/3131
Evidence: Publisher abstract describes V-I trajectory images plus active/reactive power, trajectory area and slope, fused with a lightweight dual-branch network. Evaluation uses PLAID. The original abstract reports 95.35% recognition accuracy and 0.17M parameters, but these external results are not displayed or attributed to WattSense. This is an AC waveform-based method: the current INA219 DC voltage/current telemetry does not provide synchronised AC V-I trajectories, reactive power or waveform images. The limitation is an explicit sensor/method applicability comparison, not a defect demonstrated by the paper.
[6] K. Movassagh, A. Raihan, B. Balasingam, and K. Pattipati, "A Critical Look at Coulomb Counting Approach for State of Charge Estimation in Batteries," Energies, vol. 14, no. 14, Art. 4074, 2021, doi: 10.3390/en14144074.
https://doi.org/10.3390/en14144074
Evidence: Separates current-measurement, integration, capacity and timing errors. Its results do not establish a WattSense SOC accuracy figure. Calibration/initialization is our design implication.
[7] C. Zhang, W. Allafi, Q. Dinh, P. Ascencio, and J. Marco, "Online estimation of battery equivalent circuit model parameters and state of charge using decoupled least squares technique," Energy, vol. 142, pp. 678–688, 2018, doi: 10.1016/j.energy.2017.10.043.
https://doi.org/10.1016/j.energy.2017.10.043
Evidence: Published in 2018 despite 2017 in DOI. Supports caution about fixed assumed plant parameters. WattSense has not implemented this estimator or measured its pack parameters.
[8] A. Gismero, E. Schaltz, and D.-I. Stroe, "Recursive State of Charge and State of Health Estimation Method for Lithium-Ion Batteries Based on Coulomb Counting and Open Circuit Voltage," Energies, vol. 13, no. 7, Art. 1811, 2020, doi: 10.3390/en13071811.
https://doi.org/10.3390/en13071811
Evidence: Tested aged cells with changing current/temperature. The paper explicitly identifies insufficient relaxation as a capacity-estimation issue. Our LFP pack cannot inherit its NMC OCV map or accuracy.
[9] K. Yang, Y. Tang, and Z. Zhang, "Parameter Identification and State-of-Charge Estimation for Lithium-Ion Batteries Using Separated Time Scales and Extended Kalman Filter," Energies, vol. 14, no. 4, Art. 1054, 2021, doi: 10.3390/en14041054.
https://doi.org/10.3390/en14041054
Evidence: The result is specific to its datasets and estimator. It informs future characterization; WattSense currently uses a simpler current-integration policy, not the published RLS/EKF method.
[10] B. Rzepka, S. Bischof, and T. Blank, "Implementing an Extended Kalman Filter for SoC Estimation of a Li-Ion Battery with Hysteresis: A Step-by-Step Guide," Energies, vol. 14, no. 13, Art. 3733, 2021, doi: 10.3390/en14133733.
https://doi.org/10.3390/en14133733
Evidence: Conclusions compare systematic and rough filter tuning. This is a future-estimator reference, not evidence that WattSense's INA219/current integration achieves the paper's accuracy.
[11] B. Zine, H. Bia, A. Benmouna, M. Becherif, and M. Iqbal, "Experimentally Validated Coulomb Counting Method for Battery State-of-Charge Estimation under Variable Current Profiles," Energies, vol. 15, no. 21, Art. 8172, 2022, doi: 10.3390/en15218172.
https://doi.org/10.3390/en15218172
Evidence: The broad Li-ion discussion in the abstract must not be mistaken for our 4S LFP validation. Initial SOC and suitable measurements are needed; this study is a practical procedure reference.
[12] Hend M. Fahmy, Rania A. Swief, Hany M. Hasanien, Mohammed Alharbi, José Luis Maldonado, and Francisco Jurado, "Hybrid State of Charge Estimation of Lithium-Ion Battery Using the Coulomb Counting Method and an Adaptive Unscented Kalman Filter", Energies, vol. 16, no. 14, Art. 5558, 2023, doi: 10.3390/en16145558.
https://doi.org/10.3390/en16145558
Evidence: The abstract explicitly labels numerical simulations and describes parameter fitting with African Vultures Optimization. The table includes only the estimator core. Do not present this as a physical WattSense comparison.
[13] M. Wang, G. Wang, Z. Xiao, Y. Sun, and Y. Zheng, "State of Charge Estimation of LiFePO4 in Various Temperature Scenarios," Batteries, vol. 9, no. 1, Art. 43, 2023, doi: 10.3390/batteries9010043.
https://doi.org/10.3390/batteries9010043
Evidence: Direct chemistry relevance. Temperature-dependent capacity and the flat OCV region motivate measuring the actual pack instead of relying on the assumed teaching curve. WattSense's fixed-temperature simulation does not reproduce these tests.
[14] H. Turkmanović, I. Popović, and V. Rajović, "Toward Energy Efficient Battery State of Charge Estimation on Embedded Platforms," Electronics, vol. 13, no. 21, Art. 4256, 2024, doi: 10.3390/electronics13214256.
https://doi.org/10.3390/electronics13214256
Evidence: Contrasts Rint and second-order RC EKFs and connects estimator rate to energy cost. Its reported savings cannot be copied to the ESP32; our 0.8 W controller load remains an assumption awaiting measurement.
[15] S. Bampi, G. Waltrich, and A. Vaccari, "Electronic Load for Parameter Characterization in Equivalent Circuit Models of Lithium-Ion Batteries," Eletrônica de Potência, vol. 30, Art. e202521, 2025, doi: 10.18618/REP.e202521.
https://doi.org/10.18618/REP.e202521
Evidence: Publisher full-text reports an ESP32 electronic-load instrument, lithium-titanate cell characterisation and EKF SOC estimation. Useful evidence for a laboratory procedure and embedded integration. Its battery chemistry, electronic-load instrument and estimator differ from the current protected-LFP/INA219 WattSense design; none of its accuracy transfers to our project.
[16] A. Marahatta, Y. Rajbhandari, A. Shrestha, A. Singh, A. Gachhadar, and A. Thapa, 'Priority-based low voltage DC microgrid system for rural electrification,' Energy Reports, vol. 7, pp. 43-51, 2021, doi: 10.1016/j.egyr.2020.11.030.
https://www.sciencedirect.com/science/article/pii/S2352484720314554
Evidence: Publisher explicitly describes experimental analysis and a low-cost SCADA implementation. Saved evidence identifies three load priorities and battery thresholds. This is close prior art, so priority shedding itself is not a new WattSense algorithm. The row states a qualitative study finding and transfers no performance percentage.
[17] Y. Rajbhandari, A. Marahatta, A. Shrestha, A. Gachhadar, A. Thapa, F. Gonzalez-Longatt, and P. Korba, 'Enhanced demand side management for solar-based isolated microgrid system: Load prioritisation and energy optimisation,' IET Smart Grid, vol. 7, no. 3, pp. 294-313, 2024, doi: 10.1049/stg2.12151.
https://ietresearch.onlinelibrary.wiley.com/doi/10.1049/stg2.12151
Evidence: Primary discussion identifies stochastic load/generation simulations, three priority levels and PSO-optimised SOC shedding points using forecasts. Cite issue year 2024 rather than online-first 2023. WattSense has not implemented or evaluated this forecasting/PSO method; the row is external context and transfers no result.
[18] L. Guo and J. Kors, Jr., 'Design of a Laboratory Scale Solar Microgrid Cyber-Physical System for Education,' Electronics, vol. 10, no. 13, Art. 1562, 2021, doi: 10.3390/electronics10131562.
https://www.mdpi.com/2079-9292/10/13/1562
Evidence: Primary paper reports a solar panel, purchased MPPT controller, rechargeable battery, relay-controlled loads and student assessment. Hardware data were sampled every ten minutes in its reported outdoor run. Its focus is educational system integration; it does not establish the proposed WattSense signature estimator or any WattSense measurement.
[19] E. Yusubov and L. Bekirova, 'A standalone DC microgrid energy management strategy using the battery state of charge,' Informatyka, Automatyka, Pomiary w Gospodarce i Ochronie Środowiska, vol. 13, no. 3, pp. 75-78, 2023, doi: 10.35784/iapgos.5320.
https://ph.pollub.pl/index.php/iapgos/en/article/view/5320
Evidence: The publisher abstract explicitly combines available-source power, demand and SOC with load-shedding capability and evaluates an algorithm by simulation. Although authors claim battery-life benefits, the row deliberately uses SOC-limit coordination and does not present lifetime extension as measured cycling data.
[20] J. A. Basantes, D. E. Paredes, J. R. Llanos, D. E. Ortiz, and C. D. Burgos, 'Energy Management System (EMS) Based on Model Predictive Control (MPC) for an Isolated DC Microgrid,' Energies, vol. 16, no. 6, Art. 2912, 2023, doi: 10.3390/en16062912.
https://www.mdpi.com/1996-1073/16/6/2912
Evidence: Metadata/byline was confirmed from the primary published PDF hosted in a research repository. The study compares with/without EMS under radiation and demand disturbances. Its conclusions explicitly defer battery-degradation modeling and diesel-start constraints to future work. Real-time feedback here is within the simulated coupled control system; do not call it real hardware measurement.
Sources

## Slide 14: Thank You Questions and Discussion
14
WattSense
Energy Signature Analysis and Battery Runtime Estimation
Notes: Our central idea is to connect measured load signatures with energy use and battery backup. Current Review 3 evidence is the monitoring, estimation-software, CAD and model foundation. Next is a calibrated prototype, measured known-load dataset and independent evaluation. The trained matching stage will recognise selected loads and report unknown/ambiguous cases.
Sources