## Slide 1
KJEI’s, Trinity Academy of Engineering
Department of Electronics and
Telecommunication Engineering
Academic Year 2026–27 Semester I
Project Review 3
1
    Name of Students
    Dhanesh Chaudhari (4114)
    Yash Ahire (4101)
    Mrudula Pagar (4212)
    Ujjwal Kshirsagar (4154)
Date: 3 October 2026
WattSense
Household Energy Signatures and Backup Runtime Estimation
Under the guidance of
Mahesh Sapte
Group 7
Notes: WattSense targets selected household AC appliance signatures and energy estimation, with a separate DC battery/UPS subsystem for backup-time estimation. Group 7: Dhanesh Chaudhari 4114, Yash Ahire 4101, Mrudula Pagar 4212 and Ujjwal Kshirsagar 4154. Guide: Mahesh Sapte. Review 3: 3 October 2026. The present deliverables are monitoring software, synthetic/model records and an unbuilt DC PCB design. AC metering, a measured appliance dataset, classifier training and measured backup validation remain development work.
Sources
User-confirmed expanded AC/DC scope and team details, 3 October 2026
sih 2026 shubham.pptx

## Slide 2
2
Introduction and Topic Overview
An energy signature is an appliance’s electrical power pattern over time.
Household appliances receive AC; a battery or UPS stores DC energy.
Learn selected appliance signatures and estimate their energy use.
Combine battery energy and demand to estimate available backup time.
Connect AC metering and DC battery data through a local dashboard.
Review 3: DC monitoring software and PCB design prepared.
Next stage: AC metering, signature training and measured validation.
Notes: The primary application is household appliance energy estimation. Household sockets provide AC; batteries store DC, so these require different acquisition paths. The main AC experiment first measures one selected appliance per session, then attempts controlled combinations. Recognition after training does not imply universal zero-configuration identification. The existing ESP32 firmware and local dashboard provide a DC monitoring foundation; neither currently acquires household AC data nor outputs trained appliance identities. AC identification/energy measurements can be developed while battery/inverter integration is still pending. The AC frontend must measure real power and energy through a documented protected sensing arrangement and isolated low-voltage data interface. A bare metering IC is not an isolated or enclosed meter.
Sources
sih 2026 shubham.pptx
firmware/src/main.cpp
wattsense/server.py
https://www.analog.com/en/products/ade9153a.html

## Slide 3
3
Literature Survey 1 of 4
No | Research Paper / Author / Year | Problem | Method | Data / tests | Finding | Scope limit
1 | A Scalable Real-Time Non-Intrusive Load Monitoring System for the Estimation of Household Appliance Power Consumption Athanasiadis et al., 2021 | Load energy estimation | Events + CNN + power estimate | Reported experimental evaluation | Real-time consumption estimates | Transient data needed
2 | Explainability-Informed Feature Selection and Performance Prediction for Nonintrusive Load Monitoring Mollel et al., 2023 | Unclear load classification | Decision trees + explanations | REFIT to UK-DALE transfer tests | Feature selection improves classification | Cross-house transfer needs testing
3 | Machine Learning Models for Non-Intrusive Load Monitoring: A Systematic Review and Meta-Analysis Jaime et al., 2026 | Variable evaluation methods | PRISMA + meta-analysis | 30 studies; 2017-2024 publications | Performance varies across study settings | Heterogeneous study methods
4 | Non-Intrusive Load Monitoring: A Systematic Review of Methods, Scenario-Specific Challenges, and Pathways to Practical Deployment Xiang et al., 2026 | Practical deployment barriers | Event/state methods; scenario review | Review of published NILM studies | Maps deployment needs and trade-offs | Unknown loads and transfer limits
5 | A Non-Intrusive Load Identification Method Based on the Fusion of Steady-State Features and Lightweight Network Li et al., 2026 | Similar load signatures | AC V-I + dual-branch network | PLAID AC appliance recordings | Feature fusion aids classification | Requires AC waveforms
Notes: These papers inform the proposed project. Findings belong to the cited authors and are not WattSense results. Scope limits describe applicability to the proposed AC signature and DC battery subsystems.
Li et al. use captured AC voltage-current trajectories. A low-rate RMS/real-power meter alone does not provide those waveforms; the planned first classifier uses slow power features appropriate to the selected meter.
[1] Christos Athanasiadis, Dimitrios Doukas, Theofilos Papadopoulos, Antonios Chrysopoulos, "A Scalable Real-Time Non-Intrusive Load Monitoring System for the Estimation of Household Appliance Power Consumption", Energies, vol. 14, no. 3, Art. 767, 2021, doi: 10.3390/en14030767.
https://www.mdpi.com/1996-1073/14/3/767
Evidence: Primary publisher abstract states three blocks: event detection, CNN classifier and power estimator using active-power turn-on transients. It reports computational/memory efficiency qualitatively. Cached full-page excerpt ends within the introduction, so dataset names, exact sampling rates and numerical performance are not asserted. The limitation cell is an applicability inference: this method needs suitable transient measurements and an already trained target-appliance classifier. It does not validate WattSense, universal detection or zero-configuration deployment.
[2] Rachel Stephen Mollel, Lina Stankovic, Vladimir Stankovic, "Explainability-Informed Feature Selection and Performance Prediction for Nonintrusive Load Monitoring", Sensors, vol. 23, no. 10, Art. 4845, 2023, doi: 10.3390/s23104845.
https://www.mdpi.com/1424-8220/23/10/4845
Evidence: Publisher abstract describes interpretable decision-tree classification, local/global feature importance, REFIT training and unseen same-house/UK-DALE-house evaluation. It reports class-specific improvements, but the displayed row deliberately transfers no percentage to WattSense. Cross-house transfer testing is a design implication drawn from the study setting; the current DC INA219 system cannot inherit its household-data performance.
[3] Herman Cristiano Jaime, Adler Diniz de Souza, Raphael Carlos Santos Machado, Otávio de Souza Martins Gomes, "Machine Learning Models for Non-Intrusive Load Monitoring: A Systematic Review and Meta-Analysis", Inventions, vol. 11, no. 2, Art. 29, 2026, doi: 10.3390/inventions11020029.
https://www.mdpi.com/2411-5134/11/2/29
Evidence: This is a systematic review and meta-analysis, not a new hardware trial. The publisher abstract states 30 eligible studies, random-effects pooling of F1 scores and substantial heterogeneity. Hybrid models had high pooled scores with limited study support; traditional models had broader validation. No pooled score is used as a WattSense result. Issue citation year is 2026; covered primary-study period is 2017-2024.
[4] Haotian Xiang, Wenjing Su, Yi Zong, "Non-Intrusive Load Monitoring: A Systematic Review of Methods, Scenario-Specific Challenges, and Pathways to Practical Deployment", Energies, vol. 19, no. 8, Art. 1883, 2026, doi: 10.3390/en19081883.
https://www.mdpi.com/1996-1073/19/8/1883
Evidence: This is a systematic review/framework, not new hardware validation. Its abstract explicitly identifies real-time/accuracy trade-offs, privacy, unknown loads, behaviour modelling, data quality, transferability, integration and cost. The row is a qualitative synthesis and does not assert a dataset, new classifier or measured accuracy for this review. Relevant to scoping a small known-load prototype with an unknown/ambiguous output.
[5] Yiran Li, Yan Li, Peng Han, "A Non-Intrusive Load Identification Method Based on the Fusion of Steady-State Features and Lightweight Network", Energies, vol. 19, no. 13, Art. 3131, 2026, doi: 10.3390/en19133131.
https://www.mdpi.com/1996-1073/19/13/3131
Evidence: Publisher abstract describes V-I trajectory images plus active/reactive power, trajectory area and slope, fused with a lightweight dual-branch network. Evaluation uses PLAID. The original abstract reports 95.35% recognition accuracy and 0.17M parameters, but these external results are not displayed or attributed to WattSense. This is an AC waveform-based method: the current INA219 DC voltage/current telemetry does not provide synchronised AC V-I trajectories, reactive power or waveform images. The limitation is an explicit sensor/method applicability comparison, not a defect demonstrated by the paper.
Sources

## Slide 4
4
Literature Survey 2 of 4
No | Research Paper / Author / Year | Problem | Method | Data / tests | Finding | Scope limit
6 | A Critical Look at Coulomb Counting Approach for State of Charge Estimation in Batteries Movassagh et al., 2021 | SOC error build-up | Analytical error decomposition | Error models and simulations | Quantifies four SOC error sources | Current and initial-SOC errors
7 | Online estimation of battery equivalent circuit model parameters and state of charge using decoupled least squares technique Zhang et al., 2018 | Changing battery model parameters | Decoupled weighted RLS | Lithium-ion cell measurements | Separates fast / slow dynamics | Actual pack data needed
8 | Recursive State of Charge and State of Health Estimation Method for Lithium-Ion Batteries Based on Coulomb Counting and Open Circuit Voltage Gismero et al., 2020 | Charge drift and capacity aging | Coulomb counting, OCV reset, RLS | Aged NMC cells; dynamic loads | OCV resets limit accumulated drift | Rest time and chemistry matter
9 | Parameter Identification and State-of-Charge Estimation for Lithium-Ion Batteries Using Separated Time Scales and Extended Kalman Filter Yang et al., 2021 | SOC and parameter coupling | Separated RLS + EKF | 18650 data at varied temperature | Lower error than conventional RLS | Needs characterized model and data
10 | Implementing an Extended Kalman Filter for SoC Estimation of a Li-Ion Battery with Hysteresis: A Step-by-Step Guide Rzepka et al., 2021 | Empirical tuning and sensor noise | Circuit + hysteresis + EKF tuning | Cell estimator experiment | Tuning improves estimator stability | Needs noise estimates
Notes: These papers inform the proposed project. Findings belong to the cited authors and are not WattSense results. Scope limits describe applicability to the proposed AC signature and DC battery subsystems.
Battery and microgrid studies provide subsystem context. Their particular chemistry, hardware, results and sampling cannot be transferred directly to the proposed household system.
[6] K. Movassagh, A. Raihan, B. Balasingam, and K. Pattipati, "A Critical Look at Coulomb Counting Approach for State of Charge Estimation in Batteries," Energies, vol. 14, no. 14, Art. 4074, 2021, doi: 10.3390/en14144074.
https://doi.org/10.3390/en14144074
Evidence: Separates current-measurement, integration, capacity and timing errors. Its results do not establish a WattSense SOC accuracy figure. Calibration/initialization is our design implication.
[7] C. Zhang, W. Allafi, Q. Dinh, P. Ascencio, and J. Marco, "Online estimation of battery equivalent circuit model parameters and state of charge using decoupled least squares technique," Energy, vol. 142, pp. 678–688, 2018, doi: 10.1016/j.energy.2017.10.043.
https://doi.org/10.1016/j.energy.2017.10.043
Evidence: Published in 2018 despite 2017 in DOI. Supports caution about fixed assumed plant parameters. WattSense has not implemented this estimator or measured its pack parameters.
[8] A. Gismero, E. Schaltz, and D.-I. Stroe, "Recursive State of Charge and State of Health Estimation Method for Lithium-Ion Batteries Based on Coulomb Counting and Open Circuit Voltage," Energies, vol. 13, no. 7, Art. 1811, 2020, doi: 10.3390/en13071811.
https://doi.org/10.3390/en13071811
Evidence: Tested aged cells with changing current/temperature. The paper explicitly identifies insufficient relaxation as a capacity-estimation issue. Our LFP pack cannot inherit its NMC OCV map or accuracy.
[9] K. Yang, Y. Tang, and Z. Zhang, "Parameter Identification and State-of-Charge Estimation for Lithium-Ion Batteries Using Separated Time Scales and Extended Kalman Filter," Energies, vol. 14, no. 4, Art. 1054, 2021, doi: 10.3390/en14041054.
https://doi.org/10.3390/en14041054
Evidence: The result is specific to its datasets and estimator. It informs future characterization; WattSense currently uses a simpler current-integration policy, not the published RLS/EKF method.
[10] B. Rzepka, S. Bischof, and T. Blank, "Implementing an Extended Kalman Filter for SoC Estimation of a Li-Ion Battery with Hysteresis: A Step-by-Step Guide," Energies, vol. 14, no. 13, Art. 3733, 2021, doi: 10.3390/en14133733.
https://doi.org/10.3390/en14133733
Evidence: Conclusions compare systematic and rough filter tuning. This is a future-estimator reference, not evidence that WattSense's INA219/current integration achieves the paper's accuracy.
Sources

## Slide 5
5
Literature Survey 3 of 4
No | Research Paper / Author / Year | Problem | Method | Data / tests | Finding | Scope limit
11 | Experimentally Validated Coulomb Counting Method for Battery State-of-Charge Estimation under Variable Current Profiles Zine et al., 2022 | Simple real-time SOC estimation | Current integration | Lead-acid bench tests | Bench SOC workflow | LFP tests still needed
12 | Hybrid State of Charge Estimation of Lithium-Ion Battery Using the Coulomb Counting Method and an Adaptive Unscented Kalman Filter Fahmy et al., 2023 | SOC with changing conditions | Coulomb counting plus adaptive UKF | 2.6 Ah Panasonic simulations | Lower simulated error in comparisons | Numerical results only
13 | State of Charge Estimation of LiFePO4 in Various Temperature Scenarios Wang et al., 2023 | LFP plateau and temperature | Temperature ECM; improved EKF | LFP chamber / load tests | Includes temperature | Needs pack-specific data
14 | Toward Energy Efficient Battery State of Charge Estimation on Embedded Platforms Turkmanović et al., 2024 | Estimator energy versus accuracy | Two EKFs at varied rates | PC accuracy + STM32H7 timing | Sample-rate trade-off | ESP32 timing unknown
15 | Electronic Load for Parameter Characterization in Equivalent Circuit Models of Lithium-Ion Batteries Bampi et al., 2025 | Battery parameter testing | Electronic load + ECM / EKF | LTO cell + ESP32 rig | Parameter and SOC estimates | Different test rig
Notes: These papers inform the proposed project. Findings belong to the cited authors and are not WattSense results. Scope limits describe applicability to the proposed AC signature and DC battery subsystems.
Battery and microgrid studies provide subsystem context. Their particular chemistry, hardware, results and sampling cannot be transferred directly to the proposed household system.
[11] B. Zine, H. Bia, A. Benmouna, M. Becherif, and M. Iqbal, "Experimentally Validated Coulomb Counting Method for Battery State-of-Charge Estimation under Variable Current Profiles," Energies, vol. 15, no. 21, Art. 8172, 2022, doi: 10.3390/en15218172.
https://doi.org/10.3390/en15218172
Evidence: The broad Li-ion discussion in the abstract must not be mistaken for our 4S LFP validation. Initial SOC and suitable measurements are needed; this study is a practical procedure reference.
[12] Hend M. Fahmy, Rania A. Swief, Hany M. Hasanien, Mohammed Alharbi, José Luis Maldonado, and Francisco Jurado, "Hybrid State of Charge Estimation of Lithium-Ion Battery Using the Coulomb Counting Method and an Adaptive Unscented Kalman Filter", Energies, vol. 16, no. 14, Art. 5558, 2023, doi: 10.3390/en16145558.
https://doi.org/10.3390/en16145558
Evidence: The abstract explicitly labels numerical simulations and describes parameter fitting with African Vultures Optimization. The table includes only the estimator core. Do not present this as a physical WattSense comparison.
[13] M. Wang, G. Wang, Z. Xiao, Y. Sun, and Y. Zheng, "State of Charge Estimation of LiFePO4 in Various Temperature Scenarios," Batteries, vol. 9, no. 1, Art. 43, 2023, doi: 10.3390/batteries9010043.
https://doi.org/10.3390/batteries9010043
Evidence: Direct chemistry relevance. Temperature-dependent capacity and the flat OCV region motivate measuring the actual pack instead of relying on the assumed teaching curve. WattSense's fixed-temperature simulation does not reproduce these tests.
[14] H. Turkmanović, I. Popović, and V. Rajović, "Toward Energy Efficient Battery State of Charge Estimation on Embedded Platforms," Electronics, vol. 13, no. 21, Art. 4256, 2024, doi: 10.3390/electronics13214256.
https://doi.org/10.3390/electronics13214256
Evidence: Contrasts Rint and second-order RC EKFs and connects estimator rate to energy cost. Its reported savings cannot be copied to the ESP32; our 0.8 W controller load remains an assumption awaiting measurement.
[15] S. Bampi, G. Waltrich, and A. Vaccari, "Electronic Load for Parameter Characterization in Equivalent Circuit Models of Lithium-Ion Batteries," Eletrônica de Potência, vol. 30, Art. e202521, 2025, doi: 10.18618/REP.e202521.
https://doi.org/10.18618/REP.e202521
Evidence: Publisher full-text reports an ESP32 electronic-load instrument, lithium-titanate cell characterisation and EKF SOC estimation. Useful evidence for a laboratory procedure and embedded integration. Its battery chemistry, electronic-load instrument and estimator differ from the current protected-LFP/INA219 WattSense design; none of its accuracy transfers to our project.
Sources

## Slide 6
6
Literature Survey 4 of 4
No | Research Paper / Author / Year | Problem | Method | Data / tests | Finding | Scope limit
16 | Priority-based low voltage DC microgrid system for rural electrification Marahatta et al., 2021 | Limited rural energy supply | Priority switching + SCADA | Laboratory solar-battery microgrid | Maintains essential-load service | Three-level solar system
17 | Enhanced demand side management for solar-based isolated microgrid system: Load prioritisation and energy optimisation Rajbhandari et al., 2024 | Variable solar supply | Day-ahead forecasts + PSO | Generation / load simulations | Improves priority-load continuity | Requires forecasts and optimisation
18 | Design of a Laboratory Scale Solar Microgrid Cyber-Physical System for Education Guo & Kors, 2021 | Renewable energy teaching | Sensors, Raspberry Pi, SCADA | Outdoor rig + student tests | Integrated educational platform | No signature matching
19 | A standalone DC microgrid energy management strategy using the battery state of charge Yusubov & Bekirova, 2023 | Variable PV output and demand | Power/SOC rules + load shedding | Standalone DC microgrid simulations | Coordinates loads within SOC bounds | No physical validation reported
20 | Energy Management System (EMS) Based on Model Predictive Control (MPC) for an Isolated DC Microgrid Basantes et al., 2023 | Dispatch cost and battery limits | Hierarchical control + MPC | Simulink + FICO Xpress scenarios | Reduces simulated operating cost | Battery degradation model deferred
Notes: These papers inform the proposed project. Findings belong to the cited authors and are not WattSense results. Scope limits describe applicability to the proposed AC signature and DC battery subsystems.
Battery and microgrid studies provide subsystem context. Their particular chemistry, hardware, results and sampling cannot be transferred directly to the proposed household system.
[16] A. Marahatta, Y. Rajbhandari, A. Shrestha, A. Singh, A. Gachhadar, and A. Thapa, 'Priority-based low voltage DC microgrid system for rural electrification,' Energy Reports, vol. 7, pp. 43-51, 2021, doi: 10.1016/j.egyr.2020.11.030.
https://www.sciencedirect.com/science/article/pii/S2352484720314554
Evidence: Publisher explicitly describes experimental analysis and a low-cost SCADA implementation. Saved evidence identifies three load priorities and battery thresholds. This is close prior art, so priority shedding itself is not a new WattSense algorithm. The row states a qualitative study finding and transfers no performance percentage.
[17] Y. Rajbhandari, A. Marahatta, A. Shrestha, A. Gachhadar, A. Thapa, F. Gonzalez-Longatt, and P. Korba, 'Enhanced demand side management for solar-based isolated microgrid system: Load prioritisation and energy optimisation,' IET Smart Grid, vol. 7, no. 3, pp. 294-313, 2024, doi: 10.1049/stg2.12151.
https://ietresearch.onlinelibrary.wiley.com/doi/10.1049/stg2.12151
Evidence: Primary discussion identifies stochastic load/generation simulations, three priority levels and PSO-optimised SOC shedding points using forecasts. Cite issue year 2024 rather than online-first 2023. WattSense has not implemented or evaluated this forecasting/PSO method; the row is external context and transfers no result.
[18] L. Guo and J. Kors, Jr., 'Design of a Laboratory Scale Solar Microgrid Cyber-Physical System for Education,' Electronics, vol. 10, no. 13, Art. 1562, 2021, doi: 10.3390/electronics10131562.
https://www.mdpi.com/2079-9292/10/13/1562
Evidence: Primary paper reports a solar panel, purchased MPPT controller, rechargeable battery, relay-controlled loads and student assessment. Hardware data were sampled every ten minutes in its reported outdoor run. Its focus is educational system integration; it does not establish the proposed WattSense signature estimator or any WattSense measurement.
[19] E. Yusubov and L. Bekirova, 'A standalone DC microgrid energy management strategy using the battery state of charge,' Informatyka, Automatyka, Pomiary w Gospodarce i Ochronie Środowiska, vol. 13, no. 3, pp. 75-78, 2023, doi: 10.35784/iapgos.5320.
https://ph.pollub.pl/index.php/iapgos/en/article/view/5320
Evidence: The publisher abstract explicitly combines available-source power, demand and SOC with load-shedding capability and evaluates an algorithm by simulation. Although authors claim battery-life benefits, the row deliberately uses SOC-limit coordination and does not present lifetime extension as measured cycling data.
[20] J. A. Basantes, D. E. Paredes, J. R. Llanos, D. E. Ortiz, and C. D. Burgos, 'Energy Management System (EMS) Based on Model Predictive Control (MPC) for an Isolated DC Microgrid,' Energies, vol. 16, no. 6, Art. 2912, 2023, doi: 10.3390/en16062912.
https://www.mdpi.com/1996-1073/16/6/2912
Evidence: Metadata/byline was confirmed from the primary published PDF hosted in a research repository. The study compares with/without EMS under radiation and demand disturbances. Its conclusions explicitly defer battery-degradation modeling and diesel-start constraints to future work. Real-time feedback here is within the simulated coupled control system; do not call it real hardware measurement.
Sources

## Slide 7
7
Research Gap / Problem Identification
Published recognition results depend on sensors, sampling rate and dataset.
Household appliance profiles can overlap or change across operating states.
Unseen appliances and ambiguous combinations require an UNKNOWN response.
Backup estimates depend on usable battery energy and inverter losses.
Evaluate the complete AC/DC measurement chain and estimation errors.
Proposed contribution: link household appliance signatures, energy use and available backup.
Notes: The expanded scope keeps household AC appliance estimation central and DC battery monitoring as a supporting subsystem. NILM and battery monitoring are established prior work. The academic contribution is a reproducible implementation and independent evaluation of a selected-appliance system, not a claim of a new universal recognition algorithm. Similar power signatures, different operating states and simultaneous transitions can make aggregate attribution non-identifiable. Report UNKNOWN/ambiguous results. A high Random Forest probability alone is not proof that an unseen appliance belongs to a known class. Start with controlled individual recordings before mixtures; report inference uncertainty and reference measurements separately. Slow AC-meter telemetry must not be described as harmonic or V-I waveform sensing.
Sources
.analysis/review3-signature/literature.json: Athanasiadis, Mollel, Jaime, Xiang and Li
https://scikit-learn.org/stable/modules/generated/sklearn.ensemble.RandomForestClassifier.html

## Slide 8
8
Problem Statement
Objectives
Develop a system that learns household AC appliance signatures, estimates their energy consumption, and combines DC battery data with demand to estimate backup runtime.
Measure AC real power and suitable DC battery signals.
Build labelled profiles for 4–6 selected household appliances.
Compare Random Forest, Decision Tree and profile matching.
Estimate appliance energy and backup runtime, with uncertainty.
Test unseen loads and errors on independent recording sessions.
Notes: Recognition is a planned supervised-learning task. Random Forest in local Python is the initial candidate; compare it with a Decision Tree and a transparent profile-matching baseline before choosing on independent data. Labels must be the actual connected appliance and operating state. Training/tuning/test groups are whole recording sessions, not neighbouring windows. The initial 4–6 appliance types must match the selected AC meter and supervised test setup ratings; products are not selected yet. Individual-appliance readings establish profiles and ground truth. Aggregate per-appliance Wh is a later inferred result and must be evaluated against separately metered references. AC energy estimates integrate measured real power, not apparent power. Runtime uses a qualified battery energy basis and appropriate demand measurement.
Sources
https://scikit-learn.org/stable/modules/generated/sklearn.ensemble.RandomForestClassifier.html
https://scikit-learn.org/stable/modules/generated/sklearn.model_selection.GroupKFold.html
.analysis/review3-signature/literature.json

## Slide 9
9
Proposed System Architecture
Household AC metering and a separately rated DC battery path
AC meter
Real W / Wh
RMS voltage / current
ESP32 / local Python
Features + RF candidate
Known / UNKNOWN
Load-energy estimate
Measured total +
inferred appliance Wh
Isolated data
Battery / UPS monitor
Rated sensor / telemetry
Usable Wh + DC demand
Backup estimator
Battery-side demand
or inverter-loss model
Local dashboard
Appliance, energy
and backup estimates
AC demand
Prepared: DC sensing firmware, local dashboard and unbuilt Rev B CAD.
Proposed: AC meter/interface, signature model and rated backup integration.
Notes: This diagram describes proposed information flow, not a mains wiring diagram. AC source or inverter output feeds an appropriately rated enclosed AC metering arrangement and selected household appliances. Use a documented isolated data interface to the ESP32/USB/local Python system. CT current sensing alone does not measure real power; the meter also needs an appropriate voltage reference. RMS voltage x RMS current is apparent power; active energy requires real power integration or qualified meter Wh registers. Optional PF features depend on the selected meter. ADE9153A is cited only as an example of AC metrology capability, not the chosen component or a claim that a bare chip has isolation.
The existing Rev B PCB uses non-isolated INA219 channels and is limited to a 2 A battery path and a 1.5 A continuous 5 V rail. It cannot connect to mains or carry a typical household inverter battery current. A final backup experiment needs a separately rated sensor covering the whole battery discharge/charge path, or trustworthy UPS telemetry and independently established usable energy. Bypassing the inverter around Rev B means its U1 does not see whole-pack current and cannot estimate whole-pack SOC. The existing DC board remains a bounded low-power battery bench/firmware foundation; four layers do not increase its current or voltage ratings.
Runtime is approximately usable battery Wh / mean battery-side demand W under a stated load profile and normal reserve/cutoff endpoint. If battery-side demand is measured, inverter loss and idle consumption are already included and must not be added again. If demand is inferred from AC power, use a documented conversion-loss/idle model with clear efficiency definitions. Never assume the proposed LiFePO4 pack is compatible with a lead-acid UPS charger. Use a documented compatible borrowed UPS/inverter system first. Main AC identification works without an available backup battery; backup output remains unavailable until its reference/data are valid. AC acquisition and this combined estimator are not yet implemented.
Sources
hardware/REFERENCE_WIRING.md
hardware/PCB_REQUIREMENTS.md
firmware/include/config.h
https://www.ti.com/product/INA219
https://www.analog.com/en/products/ade9153a.html

## Slide 10
10
Dataset / Data Collection
Data item | Collection plan
Initial dataset | 4–6 known household AC appliance types, one per run
Recorded fields | Time, RMS V/I, real W, Wh, labels; PF if provided
Conditions | Repeated modes and sessions; controlled combinations later
Features | Real-power steps, mean, variation and operating duration
Train / test split | Separate sessions for training, tuning and final testing
AC features follow the selected meter’s verified update rate.
Existing DC acquisition: nominal 10 Hz; telemetry: approximately 1 Hz.
AC data and classification accuracy remain to be measured.
Existing records demonstrate the DC monitoring foundation.
Notes: No physical AC signature dataset has been collected. First qualify a selected meter and its interface: minimum detectable real-power changes, actual update intervals, timestamps, resets, units and reference error. Select 4–6 compatible appliance types and record different operating modes and repeated sessions. The initial recognition target is one known appliance at a time. Ground truth comes from known connections and independent metering. Test unseen appliances and controlled combinations after the individual baseline. Whole sessions must be held out; ensure each known class is represented in suitable training sessions. Meter data at slow update rates cannot validate sub-cycle startup waveforms or harmonic signatures. Record calibration, meter model, sample timing, supply/UPS conditions and whether data are measured, public or synthetic. Published AC datasets may support an explicitly separate algorithm study; they do not validate our meter or hardware. The existing firmware 10 Hz / approximately 1 Hz rates apply only to the current DC path. New AC timing remains unselected and must be measured.
Sources
https://scikit-learn.org/stable/modules/generated/sklearn.model_selection.GroupKFold.html
firmware/src/main.cpp
.analysis/review3-signature/literature.json: Mollel and Xiang

## Slide 11
11
Expected Outcomes and Evaluation
Expected output | Evaluation method
Appliance recognition | Confusion matrix and macro F1 on held-out sessions
Unknown / ambiguous output | Unseen-load rejection and false acceptance
Total and inferred energy | Wh error against independent matched references
Backup-runtime estimate | Observed discharge endpoint and runtime error
AC/DC measurement quality | Calibration, update timing and missing-data checks
DC audit (30 Sep): 45 Python tests and 67 C++ assertions.
Both existing ESP32 firmware targets compiled.
AC metering, signature accuracy and backup performance
require measured validation.
Notes: The 30 September audit checks the DC/software/CAD foundation only. It is not AC metering, a trained classifier, inferred household appliance energy, or a physical UPS runtime result. Report measured aggregate energy separately from inferred appliance attribution. Validate attribution against independent per-appliance references and keep any unattributed residual visible. Use real W or independently checked Wh registers; integral Wh = sum(real W x elapsed seconds)/3600. Report confusion matrices and macro F1, unknown-load false acceptance and calibration error. Similar or overlapping profiles can remain ambiguous; do not claim arbitrary household disaggregation. For backup, qualify usable energy, whole-battery measurement coverage, capacity/reference, normal reserve/cutoff and variable demand. Compare prediction with repeated observed backup runs using the same endpoint and conditions. No accuracy, energy-saving percentage, lifetime extension or universal appliance compatibility is achieved yet.
Sources
docs/RECHECK_2026-09-30.md
docs/TEST_PLAN.md
https://www.analog.com/en/products/ade9153a.html
.analysis/review3-signature/literature.json

## Slide 12
12
Project Timeline
Period | Work and milestone
September 2026 | DC foundation: software, dashboard, PCB design and models
October 2026 | Qualify AC meter/interface; arrange compatible backup equipment
November 2026 | Record appliance sessions and compare signature models
Dec 2026–Jan 2027 | Validate inferred energy and battery/inverter runtime
Feb–Mar 2027 | Repeat experiments, analyse errors and final demonstration
Review 3: 3 October 2026
Final submission: the department’s next-semester schedule
Notes: The expanded household AC scope is the current plan. Start with AC metering and a measured selected-appliance dataset, independently of backup availability. Use the existing DC software/CAD as an engineering foundation, not proof of an AC prototype. Borrow an enclosed meter, reference instrument and documented compatible UPS/inverter where possible. Do not route a high-current inverter through the existing 2 A Rev B battery path. Select separately rated battery sensing or valid telemetry before whole-backup estimates. The budget remains below INR 10,000, but the old INR 9,700 DC allocation did not include AC metering or an inverter and does not establish affordability for this expansion. Exact delivered quotes, ratings and equipment access remain pending. Prioritise the AC energy-signature deliverable, defer solar and avoid unnecessary new custom power PCBs. The months are proposed milestones; final submission follows the department schedule.
Sources
User-authorized scope expansion, 3 October 2026
hardware/PCB_REQUIREMENTS.md
hardware/BUYING_PLAN_PUNE.md

## Slide 13
13
References
[1] Athanasiadis et al., 2021
10.3390/en14030767
[2] Mollel et al., 2023
10.3390/s23104845
[3] Jaime et al., 2026
10.3390/inventions11020029
[4] Xiang et al., 2026
10.3390/en19081883
[5] Li et al., 2026
10.3390/en19133131
[6] Movassagh et al., 2021
10.3390/en14144074
[7] Zhang et al., 2018
10.1016/j.energy.2017.10.043
[8] Gismero et al., 2020
10.3390/en13071811
[9] Yang et al., 2021
10.3390/en14041054
[10] Rzepka et al., 2021
10.3390/en14133733
[11] Zine et al., 2022
10.3390/en15218172
[12] Fahmy et al., 2023
10.3390/en16145558
[13] Wang et al., 2023
10.3390/batteries9010043
[14] Turkmanović et al., 2024
10.3390/electronics13214256
[15] Bampi et al., 2025
10.18618/REP.e202521
[16] Marahatta et al., 2021
10.1016/j.egyr.2020.11.030
[17] Rajbhandari et al., 2024
10.1049/stg2.12151
[18] Guo & Kors, 2021
10.3390/electronics10131562
[19] Yusubov & Bekirova, 2023
10.35784/iapgos.5320
[20] Basantes et al., 2023
10.3390/en16062912
Notes: [1] Christos Athanasiadis, Dimitrios Doukas, Theofilos Papadopoulos, Antonios Chrysopoulos, "A Scalable Real-Time Non-Intrusive Load Monitoring System for the Estimation of Household Appliance Power Consumption", Energies, vol. 14, no. 3, Art. 767, 2021, doi: 10.3390/en14030767.
https://www.mdpi.com/1996-1073/14/3/767
Evidence: Primary publisher abstract states three blocks: event detection, CNN classifier and power estimator using active-power turn-on transients. It reports computational/memory efficiency qualitatively. Cached full-page excerpt ends within the introduction, so dataset names, exact sampling rates and numerical performance are not asserted. The limitation cell is an applicability inference: this method needs suitable transient measurements and an already trained target-appliance classifier. It does not validate WattSense, universal detection or zero-configuration deployment.
[2] Rachel Stephen Mollel, Lina Stankovic, Vladimir Stankovic, "Explainability-Informed Feature Selection and Performance Prediction for Nonintrusive Load Monitoring", Sensors, vol. 23, no. 10, Art. 4845, 2023, doi: 10.3390/s23104845.
https://www.mdpi.com/1424-8220/23/10/4845
Evidence: Publisher abstract describes interpretable decision-tree classification, local/global feature importance, REFIT training and unseen same-house/UK-DALE-house evaluation. It reports class-specific improvements, but the displayed row deliberately transfers no percentage to WattSense. Cross-house transfer testing is a design implication drawn from the study setting; the current DC INA219 system cannot inherit its household-data performance.
[3] Herman Cristiano Jaime, Adler Diniz de Souza, Raphael Carlos Santos Machado, Otávio de Souza Martins Gomes, "Machine Learning Models for Non-Intrusive Load Monitoring: A Systematic Review and Meta-Analysis", Inventions, vol. 11, no. 2, Art. 29, 2026, doi: 10.3390/inventions11020029.
https://www.mdpi.com/2411-5134/11/2/29
Evidence: This is a systematic review and meta-analysis, not a new hardware trial. The publisher abstract states 30 eligible studies, random-effects pooling of F1 scores and substantial heterogeneity. Hybrid models had high pooled scores with limited study support; traditional models had broader validation. No pooled score is used as a WattSense result. Issue citation year is 2026; covered primary-study period is 2017-2024.
[4] Haotian Xiang, Wenjing Su, Yi Zong, "Non-Intrusive Load Monitoring: A Systematic Review of Methods, Scenario-Specific Challenges, and Pathways to Practical Deployment", Energies, vol. 19, no. 8, Art. 1883, 2026, doi: 10.3390/en19081883.
https://www.mdpi.com/1996-1073/19/8/1883
Evidence: This is a systematic review/framework, not new hardware validation. Its abstract explicitly identifies real-time/accuracy trade-offs, privacy, unknown loads, behaviour modelling, data quality, transferability, integration and cost. The row is a qualitative synthesis and does not assert a dataset, new classifier or measured accuracy for this review. Relevant to scoping a small known-load prototype with an unknown/ambiguous output.
[5] Yiran Li, Yan Li, Peng Han, "A Non-Intrusive Load Identification Method Based on the Fusion of Steady-State Features and Lightweight Network", Energies, vol. 19, no. 13, Art. 3131, 2026, doi: 10.3390/en19133131.
https://www.mdpi.com/1996-1073/19/13/3131
Evidence: Publisher abstract describes V-I trajectory images plus active/reactive power, trajectory area and slope, fused with a lightweight dual-branch network. Evaluation uses PLAID. The original abstract reports 95.35% recognition accuracy and 0.17M parameters, but these external results are not displayed or attributed to WattSense. This is an AC waveform-based method: the current INA219 DC voltage/current telemetry does not provide synchronised AC V-I trajectories, reactive power or waveform images. The limitation is an explicit sensor/method applicability comparison, not a defect demonstrated by the paper.
[6] K. Movassagh, A. Raihan, B. Balasingam, and K. Pattipati, "A Critical Look at Coulomb Counting Approach for State of Charge Estimation in Batteries," Energies, vol. 14, no. 14, Art. 4074, 2021, doi: 10.3390/en14144074.
https://doi.org/10.3390/en14144074
Evidence: Separates current-measurement, integration, capacity and timing errors. Its results do not establish a WattSense SOC accuracy figure. Calibration/initialization is our design implication.
[7] C. Zhang, W. Allafi, Q. Dinh, P. Ascencio, and J. Marco, "Online estimation of battery equivalent circuit model parameters and state of charge using decoupled least squares technique," Energy, vol. 142, pp. 678–688, 2018, doi: 10.1016/j.energy.2017.10.043.
https://doi.org/10.1016/j.energy.2017.10.043
Evidence: Published in 2018 despite 2017 in DOI. Supports caution about fixed assumed plant parameters. WattSense has not implemented this estimator or measured its pack parameters.
[8] A. Gismero, E. Schaltz, and D.-I. Stroe, "Recursive State of Charge and State of Health Estimation Method for Lithium-Ion Batteries Based on Coulomb Counting and Open Circuit Voltage," Energies, vol. 13, no. 7, Art. 1811, 2020, doi: 10.3390/en13071811.
https://doi.org/10.3390/en13071811
Evidence: Tested aged cells with changing current/temperature. The paper explicitly identifies insufficient relaxation as a capacity-estimation issue. Our LFP pack cannot inherit its NMC OCV map or accuracy.
[9] K. Yang, Y. Tang, and Z. Zhang, "Parameter Identification and State-of-Charge Estimation for Lithium-Ion Batteries Using Separated Time Scales and Extended Kalman Filter," Energies, vol. 14, no. 4, Art. 1054, 2021, doi: 10.3390/en14041054.
https://doi.org/10.3390/en14041054
Evidence: The result is specific to its datasets and estimator. It informs future characterization; WattSense currently uses a simpler current-integration policy, not the published RLS/EKF method.
[10] B. Rzepka, S. Bischof, and T. Blank, "Implementing an Extended Kalman Filter for SoC Estimation of a Li-Ion Battery with Hysteresis: A Step-by-Step Guide," Energies, vol. 14, no. 13, Art. 3733, 2021, doi: 10.3390/en14133733.
https://doi.org/10.3390/en14133733
Evidence: Conclusions compare systematic and rough filter tuning. This is a future-estimator reference, not evidence that WattSense's INA219/current integration achieves the paper's accuracy.
[11] B. Zine, H. Bia, A. Benmouna, M. Becherif, and M. Iqbal, "Experimentally Validated Coulomb Counting Method for Battery State-of-Charge Estimation under Variable Current Profiles," Energies, vol. 15, no. 21, Art. 8172, 2022, doi: 10.3390/en15218172.
https://doi.org/10.3390/en15218172
Evidence: The broad Li-ion discussion in the abstract must not be mistaken for our 4S LFP validation. Initial SOC and suitable measurements are needed; this study is a practical procedure reference.
[12] Hend M. Fahmy, Rania A. Swief, Hany M. Hasanien, Mohammed Alharbi, José Luis Maldonado, and Francisco Jurado, "Hybrid State of Charge Estimation of Lithium-Ion Battery Using the Coulomb Counting Method and an Adaptive Unscented Kalman Filter", Energies, vol. 16, no. 14, Art. 5558, 2023, doi: 10.3390/en16145558.
https://doi.org/10.3390/en16145558
Evidence: The abstract explicitly labels numerical simulations and describes parameter fitting with African Vultures Optimization. The table includes only the estimator core. Do not present this as a physical WattSense comparison.
[13] M. Wang, G. Wang, Z. Xiao, Y. Sun, and Y. Zheng, "State of Charge Estimation of LiFePO4 in Various Temperature Scenarios," Batteries, vol. 9, no. 1, Art. 43, 2023, doi: 10.3390/batteries9010043.
https://doi.org/10.3390/batteries9010043
Evidence: Direct chemistry relevance. Temperature-dependent capacity and the flat OCV region motivate measuring the actual pack instead of relying on the assumed teaching curve. WattSense's fixed-temperature simulation does not reproduce these tests.
[14] H. Turkmanović, I. Popović, and V. Rajović, "Toward Energy Efficient Battery State of Charge Estimation on Embedded Platforms," Electronics, vol. 13, no. 21, Art. 4256, 2024, doi: 10.3390/electronics13214256.
https://doi.org/10.3390/electronics13214256
Evidence: Contrasts Rint and second-order RC EKFs and connects estimator rate to energy cost. Its reported savings cannot be copied to the ESP32; our 0.8 W controller load remains an assumption awaiting measurement.
[15] S. Bampi, G. Waltrich, and A. Vaccari, "Electronic Load for Parameter Characterization in Equivalent Circuit Models of Lithium-Ion Batteries," Eletrônica de Potência, vol. 30, Art. e202521, 2025, doi: 10.18618/REP.e202521.
https://doi.org/10.18618/REP.e202521
Evidence: Publisher full-text reports an ESP32 electronic-load instrument, lithium-titanate cell characterisation and EKF SOC estimation. Useful evidence for a laboratory procedure and embedded integration. Its battery chemistry, electronic-load instrument and estimator differ from the current protected-LFP/INA219 WattSense design; none of its accuracy transfers to our project.
[16] A. Marahatta, Y. Rajbhandari, A. Shrestha, A. Singh, A. Gachhadar, and A. Thapa, 'Priority-based low voltage DC microgrid system for rural electrification,' Energy Reports, vol. 7, pp. 43-51, 2021, doi: 10.1016/j.egyr.2020.11.030.
https://www.sciencedirect.com/science/article/pii/S2352484720314554
Evidence: Publisher explicitly describes experimental analysis and a low-cost SCADA implementation. Saved evidence identifies three load priorities and battery thresholds. This is close prior art, so priority shedding itself is not a new WattSense algorithm. The row states a qualitative study finding and transfers no performance percentage.
[17] Y. Rajbhandari, A. Marahatta, A. Shrestha, A. Gachhadar, A. Thapa, F. Gonzalez-Longatt, and P. Korba, 'Enhanced demand side management for solar-based isolated microgrid system: Load prioritisation and energy optimisation,' IET Smart Grid, vol. 7, no. 3, pp. 294-313, 2024, doi: 10.1049/stg2.12151.
https://ietresearch.onlinelibrary.wiley.com/doi/10.1049/stg2.12151
Evidence: Primary discussion identifies stochastic load/generation simulations, three priority levels and PSO-optimised SOC shedding points using forecasts. Cite issue year 2024 rather than online-first 2023. WattSense has not implemented or evaluated this forecasting/PSO method; the row is external context and transfers no result.
[18] L. Guo and J. Kors, Jr., 'Design of a Laboratory Scale Solar Microgrid Cyber-Physical System for Education,' Electronics, vol. 10, no. 13, Art. 1562, 2021, doi: 10.3390/electronics10131562.
https://www.mdpi.com/2079-9292/10/13/1562
Evidence: Primary paper reports a solar panel, purchased MPPT controller, rechargeable battery, relay-controlled loads and student assessment. Hardware data were sampled every ten minutes in its reported outdoor run. Its focus is educational system integration; it does not establish the proposed WattSense signature estimator or any WattSense measurement.
[19] E. Yusubov and L. Bekirova, 'A standalone DC microgrid energy management strategy using the battery state of charge,' Informatyka, Automatyka, Pomiary w Gospodarce i Ochronie Środowiska, vol. 13, no. 3, pp. 75-78, 2023, doi: 10.35784/iapgos.5320.
https://ph.pollub.pl/index.php/iapgos/en/article/view/5320
Evidence: The publisher abstract explicitly combines available-source power, demand and SOC with load-shedding capability and evaluates an algorithm by simulation. Although authors claim battery-life benefits, the row deliberately uses SOC-limit coordination and does not present lifetime extension as measured cycling data.
[20] J. A. Basantes, D. E. Paredes, J. R. Llanos, D. E. Ortiz, and C. D. Burgos, 'Energy Management System (EMS) Based on Model Predictive Control (MPC) for an Isolated DC Microgrid,' Energies, vol. 16, no. 6, Art. 2912, 2023, doi: 10.3390/en16062912.
https://www.mdpi.com/1996-1073/16/6/2912
Evidence: Metadata/byline was confirmed from the primary published PDF hosted in a research repository. The study compares with/without EMS under radiation and demand disturbances. Its conclusions explicitly defer battery-degradation modeling and diesel-start constraints to future work. Real-time feedback here is within the simulated coupled control system; do not call it real hardware measurement.
Sources

## Slide 14: Thank You Questions and Discussion
14
WattSense
Household Energy Signatures and Backup Runtime Estimation
Notes: The primary deliverable is a measured household AC signature library and evaluated load-energy estimation. A separately rated DC battery/UPS subsystem adds backup-time estimates after qualification. The next practical milestone is a validated AC meter/interface and labelled appliance recordings, followed by baseline/model comparisons and uncertainty handling. Current AC hardware, classifier training and physical backup validation are pending.
Sources